ACE-128/64 PROGRAMMER'S REFERENCE GUIDE  (version 1.2b, for Release #11)

by Craig Bruce  <csbruce@ccnga.uwaterloo.ca>  02-Feb-1994, Rev. 21-Sep-1994.

1. INTRODUCTION

ACE is a program for the Commodore 128 and Commodore 64 that provides a
command shell environment that is similar to that of Unix.  It is still in the
development stage, but enough of it is complete to be useful.  BTW, "ACE"
means "Advanced Computing Environment" (well, advanced for the 128/64).

So what is ACE all about?  Well, originally I tried a very ambitious project
of writing a multitasking operating system for the 128.  It got it partially
working, but it was much too fragile and incomplete to be released.  It was a
white-elephant project.  So, then then it came to me that I was aiming much
too high.  What I needed was a much simpler system, one that would give the
type of programming interface and built-in features that I wanted, but one
that was close enough to the Commodore Kernal that it would not require much
of a programming effort to hack together a minimal implementation.  And thus,
there was ACE-128 Release #1.  And I saw it was good.

What I wanted was a system that would be easier to program than the Commodore
Kernal with all its weird and wonderful device types, non-existent memory
management, and single-application design.  The first important feature of
this environment was to be able to pass arguments from a command line to an
application program by typing them on the command line of the shell.  It is so
annoying to load up a program in BASIC, run it, and have it ask you for
filenames in some highly inconvenient way.

Another important system feature is to make near and far memory management
part of the system, and to make far memory convenient to use for storing
massively bulky data.  And so it was.  Also, we want to use custom device
drivers.  Commodore didn't really come through with the device drivers it
provided.  They are all REALLY SLOW.  And so that was, also, although more
custom device drivers are needed.  We want to have the capability of making
programs work together, rather than having programs that are totally
incompatible.  This functionality is still under construction.  Programs will
work together in this uni-tasking environment by allowing a program to execute
another program as a sub-task, and then having control return to the calling
program upon exit.  Finally, we want some good quality applications and a
powerful command shell.  This is still being worked on and progress is coming
slowly.  Oh, almost forgot; we also want all programs to work on both the C64
and C128, and they do.

2. SYSTEM INTERFACE

This section describes the interface between user programs and the ACE kernel.
I am very careful throughout this interface specification about revealing any
internal details that you do not strictly need to know.  The interface with
ACE is not specified in terms of absolute addresses; to aid in portability and
extensibility, all interfaces are specified in terms of symbolic assembler
labels.  All of the ACE code is currently written for the Buddy-128 assembler.
Also, because these interface absolute addresses are subject to change from
version to version of the kernel, executables compiled for use with an old
version of ACE may not work with a new version.

2.1. ZERO-PAGE VARIABLES

There are four zero-page variables used for passing arguments in most system
calls.  They are as follows:

SYMBOL   BYTES   DESCRIPTION
-------  -----   -----------
zp           2   zeropage pointer
zw           2   zeropage word
mp           4   memory pointer
syswork     16   system work area / arguments

The first two, "zp" and "zw" are used in most calls.  They store simple 16-bit
values; "zp" usually stores pointers to strings in RAM0 memory.  The "mp"
variable is 32-bits in length and is used exclusively for passing far memory
pointers for use with the far memory routines.  All three of these variables
will remain unchanged inside of system call unless they will contain a return
value.  "syswork" is a 16-byte array used mainly when there are too many
arguments for other variables to hold, and all non-input and non-output bytes
of "syswork" are subject to change by the kernel.  All input arguments placed
in the "syswork" locations will be preserved unless otherwise indicated.

2.2. SYSTEM VARIABLES

There are several non-zeropage variables for storing system status and return
values:

SYMBOL          BYTES   DESCRIPTION
----------      -----   -----------
errno               1   error number code returned by failed system calls
aceID               2   proof that user program is running on top of ACE
aceArgc             2   argument count for current process
aceArgv             2   argument vector address for current process
aceMemTop           2   highest address, plus one, that user prog can use
aceShellPath      256   storage for search path for executable programs
aceShellAlias     256   storage for shell command aliases
aceCurDirName     128   storage for the current directory name
aceExitData       256   storage for exit status from the last called prg
aceDirentBuffer <next>  storage for directory entries read from disk
aceDirentLength     -   really a constant: length in bytes of "aceDirentBuffer"
aceDirentBytes      4   bytes in file (usually inexact)
aceDirentDate       8   date of file in "YY:YY:MM:DD:HH:MM:SS:TW" format
aceDirentType       4   type of file in null-terminated string
aceDirentFlags      1   flags of file, "drwx*-et" format
aceDirentUsage      1   more flags of file, "ulshm---" format
aceDirentNameLen    1   length of name of file
aceDirentName      17   null-terminated name of file

ERRNO: "errno" is used to return error codes from system calls.  When a system
call ends in error, it sets the carry flag to "1", puts the error code in
"errno", and returns to the user program, after undoing any system work
completed at the time the error is encountered and aborting the operation.  An
error code number is stored in binary in the single-byte "errno" location. The
symbolic names for the possible error codes are given in the next section. If
no error occurs in a system call, the carry flag will be cleared on return
from the call.  Note that not all system calls can run into errors, so not all
set the carry flag accordingly.

ID: "aceID" is a two-byte variable.  Its purpose is to allow user programs to
be sure that they are executing on top of ACE.  The low byte (i.e., the first
byte) must be equal to the symbolic constant "aceID1", and the high, "aceID2".
This will allow ACE applications to inform idiot users that they cannot simply
BOOT the program from BASIC, but rather they must run ACE first.

ARGC: "aceArgc" is a two-byte unsigned number.  It gives the number of
arguments passed to the application by the program (usually the command shell)
that called the application.  The first argument is always the name of the
application program, so the count will always be at least one.  Other
arguments are optional.

ARGV: "aceArgv" is a two-byte RAM0 pointer.  Pay attention.  This pointer
points to the first entry of an array of two-byte pointers which point to the
null-terminated strings that are the arguments passed to the application
program by the caller.  (A null-terminated string is one that ends with a zero
byte).  To find the address of the N-th argument to an application, multiply N
by two, add the "aceArgv" contents to that, and fetch the pointer from that
address.  In this scheme, the ever-present application name is the 0-th
argument.  The argv[argc] element of the argument vector will always contain a
value of $0000, a null pointer.

MEM-TOP: "aceMemTop" is a two-byte RAM0 pointer.  This points to one byte past
the highest byte that the application program is allowed to use.  All
application programs are loaded into memory at address "aceAppAddress" (next
section), and all memory between the end of the progam code and "aceMemTop"
can be used for temporary variables, file buffers, etc.  The main problem with
this approach is that there are no guarantees about how much memory your
application will get to play with.  Many applications, such as simple file
utilities, can simply use all available memory for a file buffer, but other
programs, such as a file compressor, may have much greater demand for "near"
memory.

SHELL-PATH: "aceShellPath" is a 256-byte array of characters.  This stores the
pathnames of directories to search through in order to find executable files.
Each pathname is stored as a null-terminated string, and the list is
terminated by an empty string (containing only the zero character).  This is
intended to be used by the shell program, or any other program that is so
inclined, to examine or alter the search path.  The search paths specified in
the path page are global variables and are used by all programs that make the
"exec" system call.  This mechanism for reading/altering the executable search
path may be changed in the future.

SHELL-ALIAS: "aceShellAlias" is a 256-byte array of characters.  This stores
the aliases to be used with the command shell.  An alias is a string that is
substituted in the place of a command name on a shell command line whenever a
certain command name comes up.  For example, you might specify if the user
enters the command "list a:" that the command name "list" be string-replaced
with "cls;xls -l".  Each alias is stored with the command name first, followed
by an equals character ("="), followed by the string to substitute, followed
by a zero.  The alias list is terminated by an empty string.  This mechanism
may be extended in the future to allow multiple pages of aliases, or may be
changed completely.

CUR-DIR-NAME: "aceCurDirName" is a 128-byte array of characters.  It contains
the null-terminated string indicating the current directory.  The user is not
supposed to modify this value, and the value will not always give a full
pathname.  The implementation of this feature may need to change in future
versions of ACE.

ACE-EXIT-DATA: "aceExitData" is a 256-byte array.  It is the 256-byte buffer
allocated for user programs to give detailed return information upon exiting
back to their parent program.  See the "exit" system call.  User programs are
allowed to read and write this storage.  An example use of this feature would
be a compiler program returning the line number and character position, and
description of a compilation error to a text editor, so the editor can
position the cursor and display the error message for user convenience.  The
implementation of this feature may need to change in future versions of ACE.

DIRENT-BUFFER: "aceDirentBuffer" is a buffer used for storing directory
information read with the "dirread" system call, and is "aceDirentLength"
bytes long.  Only a single directory entry is (logically) read from disk at a
time.  The individual fields of a read directory entry are accessed by the
fields described next.  This field is also used for returning disk name
information and the number of bytes free on a disk drive (see the "dirread"
system call).

DIRENT-BYTES: "aceDirentBytes" is a four-byte (32-bit) unsigned field.  As
always, the bytes are addressed from least significant to most significant.
This field gives the number of bytes in the file.  Note that this value may
not be exact, since Commodore decided to store sizes in disk blocks rather
than bytes.  For devices that report only block counts (i.e., every disk
device currently supported), the number of bytes returned is the number of
blocks multiplied by 254.  This field, as well and the other dirent fields are
absolute addresses, not offsets from aceDirentBuffer.

DIRENT-DATE: "aceDirentDate" is an eight-byte array of binary coded decimal
values, stored from most significant digits to least significant.  The first
byte contains the BCD century, the second the year, and so on, and the last
byte contains the number of tenths of seconds in its most significant nybble
and a code for the day-of-week in its least significant nybble.  Sunday has
code 1, Monday 2, etc., Saturday 7, and a code of 0 means "unknown".  This is
the standard format for all dates used in ACE.  This format is abstracted as
"YY:YY:MM:DD:HH:MM:SS:TW".  For disk devices that don't support dates, this
field will be set to all zeroes, which can be conveniently interpreted as the
NULL date, negative infinity, or as the time that J.C. was a seven-year-old
boy.

DIRENT-TYPE: "aceDirentType" is a three-character (four-byte) null-terminated
string.  It indicates what type the file is, in lowercase PETSCII.  Standard
types such as "SEQ" and "PRG" will be returned, as well and other
possibilities for custom device drivers.

DIRENT-FLAGS: "aceDirentFlags" is a one-byte field that is interpreted as
consisting of eight independent one-bit fields.  The abstract view of the
fields is "drwx*-et".  "d" means that the item is a subdirectory (otherwise it
is a regular file), "r" means the item is readable, "w" means the item is
writable, and "x" means the item is executable.  The "x" option is really not
supported currently.  "*" means the item is improperly closed (a "splat" file
in Commodore-DOS terminology).  The "-" field is currently undefined.  "e"
means that the value given in the "aceDirentBytes" field is actually exact,
and "t" means the file should be interpreted as being a "text" file
(otherwise, its type is either binary or unknown).  The bit fields are all
booleans; a value of "1" means true, "0", false.  The "d" bit occupies the
128-bit position, etc.

DIRENT-USAGE: "aceDirentFlags" is a one-byte field very much like
"aceDirentFlags".  The abstract view of the fields is "ulshm---".  "u"
indicates whether the directory entry is used (current) or not (deleted).
The directory system calls will not read a directory entry that is deleted, so
you will never see this bit not set; it is used internally.  "l" indicates
whether the directory entry is for an actual file (==0, normal) or a "link"
(==1) to another file.  The "s" and "h" bits indicate which type a link is:
"soft" or "hard", respectively.  These both work similarly to Unix hard and
soft links.  The "m" flag indicates whether a file has been modified since
the last time that a backup program cleared the "m" bit for the file, allowing
incremental backups.

DIRENT-NAME-LEN: "aceDirentNameLen" is a one-byte number.  It gives the number
of characters in the filename.  It is present for convenience.

DIRENT-NAME: "aceDirentName" is a 16-character (17-byte) null-terminated
character string field.  It gives the name of the file or directory or disk.
Filenames used with ACE are limited to 16 characters.

2.3. SYSTEM CONSTANTS

There are several symbolic constants that are used with the ACE system
interface:

SYMBOL                   DESCRIPTION
-------------------      -------------------------
aceAppAddress            the start address of applications
aceID1                   the id characters used to identify ACE applications
aceID2                   ...
aceID3                   ...
aceMemNull               the far memory type code used to indicate null ptrs
aceMemREU                far mem type code for Ram Expansion Unit memory
aceMemInternal           far mem type code for internal memory
aceMemRLREU              far mem type code for REU memory accessed thru RAMLink
aceMemRL                 far mem type code for direct-access RAMLink memory
aceErrStopped            error code for syscall aborted by STOP key
aceErrTooManyFiles       err: too many files already opened to open another
aceErrFileOpen           err: don't know what this means
aceErrFileNotOpen        err: the given file descriptor is not actually open
aceErrFileNotFound       err: named file to open for reading does not exist
aceErrDeviceNotPresent   err: the specified physical device is not online
aceErrFileNotInput       err: file cannot be opened for reading
aceErrFileNotOutput      err: file cannot be opened for writing
aceErrMissingFilename    err: pathname component is the null string
aceErrIllegalDevice      err: the specified device cannot do what you want
aceErrWriteProtect       err: trying to write to a disk that is write-protected
aceErrFileExists         err: trying to open for writing file that exists
aceErrFileTypeMismatch   err: you specified the file type incorrectly
aceErrNoChannel          err: too many open files on disk drive to open another
aceErrInsufficientMemory err: ACE could not allocate the memory you requested
aceErrOpenDirectory      err: you are trying to open a dir as if it were a file
aceErrDiskOnlyOperation  err: trying to perform disk-only op on char device
aceErrNullPointer        err: trying to dereference a null far pointer
aceErrInvalidFreeParms   err: bad call to "pagefree": misaligned/wrong size
aceErrFreeNotOwned       err: trying to free far memory you don't own
aceErrInvalidWindowParms err: invalid window dimensions were given
aceErrInvlaidConParms    err: invalid console parameters were given
aceErrInvalidFileMode    err: opening a file for other-than "r","w", or "a"
aceErrNotImplemented     err: system call or option is not (yet) implemented
aceErrBloadTruncated     err: a bload operation stopped before exceeding limit
aceErrPermissionDenied   err: attempt to read or write a file without perms
stdin                    file descriptor reserved for stdin input stream
stdout                   file descriptor reserved for stdout output stream
stderr                   file descriptor reserved for stderr output stream

"aceAppAddress", as discussed before, is the address that application programs
are loaded into memory at.  They must, of course, be compiled to execute
starting at this address.

The "aceMem" group of constants are for use with the "pagealloc" system call,
except for "aceMemNull", which may be used by application programs for
indicating null far pointers.  The "pagealloc" call allows you to specify what
types of memory you are willing to accept.  This is important because the
difference types of memory have different performance characteristics.  ACE
will try to give you the fastest memory that is available.  Ram Expansion Unit
memory has startup and byte-transfer times of about 60 us (microseconds) and 1
us, respectively.  This is the fastest type of far memory.  Internal memory
has a startup time of 24 us and a byte-transfer time of between 7 and 14 us
(depending on whether accessing RAM0 or RAM1+).  REU memory accessed through a
RAMLink has a terrible startup time of 1000 us and a byte-transfer time of 2
us.  Direct-access RAMLink memory has a startup time of 1000 us and a
byte-transfer time of 16 us.  All these times are for the C128 in 2 MHz mode.

The "aceErr" group gives the error codes returned by system calls.  The error
codes are returned in the "errno" variable.  Not all possible error codes from
Commodore disk drives are covered, but the important ones are.  Finally, the
"std" files group give the symbolic file descriptor identifiers of the default
input, output, and error output file streams.

2.4. SYSTEM CALLS

All system calls are called by setting up arguments in specified processor
registers and memory locations, executing a JSR to the system call address,
and pulling the return values out of processor registers and memory locations.

2.4.1. FILE CALLS

NAME   :  open
PURPOSE:  open a file
ARGS   :  (zp) = pathname
          .A   = file mode ("r", "w", or "a")
RETURNS:  .A   = file descriptor number
          .CS  = error occurred flag
ALTERS :  .X, .Y, errno

Opens a file.  The name of the file is given by a pointer to a null-terminated
string, and may contain device names and pathnames as specified in the ACE
user documentation.  The file mode is a PETSCII character.  "r" means to open
the file for reading, "w" means to open the file for writing, and "a" means to
open the file for appending (writing, starting at the end of the file).  An
error will be returned if you attempt to open for reading or appending a file
that does not exist, or if you attempt to open for writing a file that does
already exist.  If you wish to overwrite an existing file, you will have to
call "remove" to delete the old version before opening the new version for
writing.

The function returns a file descriptor number, which is a small unsigned
integer that is used with other file calls to specify the file that has been
opened.  File descriptors numbered 0, 1, and 2 are used for stdin, stdout, and
stderr, respectively.  The file descriptor returned will be the minimum number
that is not currently in use.  These numbers are system-wide (rather than
local to a process as in Unix), and this has some implications for I/O
redirection (see the "fdswap" call below).

Restrictions: only so many Kernal files allowed to be open on a disk device,
and there is a system maximum of open files.  You will get a "too many files"
error if you ever exceed this limit.  Also, because of the nature of
Commodore-DOS, there may be even tighter restrictions on the number of files
that can be simultaneously open on a single disk device, resulting in a "no
channel" error.  Note that this call checks the status channel of Commodore
disk drives on each open, so you don't have to (and should not anyway).

If the current program exits either by calling "exit" or simply by doing the
last RTS, all files that were opened by the program and are still open will be
automatically closed by the system before returning to the parent program.

NAME   :  close
PURPOSE:  close an open file
ARGS   :  .A   = File descriptor number
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Closes an open file.  Not much to say about this one.

NAME   :  read
PURPOSE:  read data from an open file
ARGS   :  .X   = File descriptor number
          (zp) = pointer to buffer to store data into
          .AY  = maximum number of bytes to read
RETURNS:  .AY  = (zw) = number of bytes actually read in
          .CS  = error occurred flag
          .ZS  = EOF reached flag
ALTERS :  .X, errno

Reads data from the current position of an open file.  Up to the specified
maximum number of bytes will be read.  You should not give a maximum of zero
bytes, or you may misinterpret an EOF (end of file).  The buffer must be at
least the size of the maximum number of bytes to read.  The data are not
interpreted in any way, so it is the programmer's responsibility to search for
carriage return characters to locate lines of input, if he so desires.
However, for the console the input is naturally divided up into lines, so each
call will return an entire line of bytes if the buffer is large enough.  There
are no guarantees about the number of bytes that will be returned, except that
it will be between 1 and the buffer size.  So, if you wish to read a certain
number of bytes, you may have to make multiple read calls.

The call returns the number of bytes read in both the .AY register pair and in
(zw), for added convenience.  A return of zero bytes read means that the end
of the file has been reached.  An attempt to read beyond the end of file will
simply give another EOF return.  End of file is also returned in the .Z flag
of the processor.

NAME   :  write
PURPOSE:  write data to an open file
ARGS   :  .X   = file descriptor number
          (zp) = pointer to data to be written
          .AY  = length of data to be written in bytes
RETURNS:  .CS  = error occurred
ALTERS :  .A, .X, .Y, errno

Writes data at the current position of an open file.  'Nuff said.

NAME   :  fastopen
PURPOSE:  open a file for fast reading
ARGS   :  (zp) = Name
          .A   = file mode (must be "r")
RETURNS:  .A   = file descriptor number
          .CS  = error occurred flag
ALTERS :  .X, .Y, errno

This performs the same function as the regular "open" call, except this style
of file accessing will allow files to be read much faster than the other.  On
devices that are so equipped, the "fastload" burst command is used (similar
shortcuts may be possible with other devices too).  The drawback of this
increased speed is that no other device I/O can take place while a file is
opened for "fast" access, not even to other devices, except for output to the
console.  Other files can be open, just not accessed.  You also cannot open
more than one "fast" file at a time.  Interrupts will be disabled while a file
is open for fast accessing, so the user cannot re-enable them, for technical
reasons.  The arguments to this call are exactly the same as the regular
"open" to make it easy to switch from using one to the other.  [Note: in
Release #10, these "fast" calls are simply short-circuited to the regular
file calls].

NAME   :  fastclose
PURPOSE:  close the file that was opened for fast reading
ARGS   :  .A   = File descriptor number
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Closes the file that was opened for fast reading.

NAME   :  fastread
PURPOSE:  read data from the file opened for fast reading
ARGS   :  .X   = File descriptor number
          (zp) = pointer to buffer to store data into
          .AY  = maximum number of bytes to read
RETURNS:  .AY  = (zw) = number of bytes actually read in
          .CS  = error occurred flag
          .ZS  = EOF reached flag
ALTERS :  .X, errno

Read data from the (one) file that is currently opened for "fast" reading. The
arguments and semantics are equivalent to the regular "read" call.

NAME   :  bload
PURPOSE:  binary load
ARGS   :  (zp) = pathname
          .AY  = address to load file
          (zw) = highest address that file may occupy, plus one
RETURNS:  .AY  = end address of load, plus one
          .CS  = error occurred flag
ALTERS :  .X, errno

Binary-load a file directly into memory.  If the file will not fit into the
specified space, an error will be returned and the load truncated if the
device supports truncation; otherwise, important data may be overwritten.

NAME   :  remove
PURPOSE:  delete a file
ARGS   :  (zp) = pathname
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Delete the named file.

NAME   :  rename
PURPOSE:  rename a file or directory
ARGS   :  (zp) = old filename
          (zw) = new filename
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Renames a file or directory.  If a file with the new name already exists, then
the operation will be aborted and a "file exists" error will be returned.  On
most devices, the file to be renamed must be in the current directory and the
new name may not include any path, just a filename.

NAME   :  devinfo
PURPOSE:  give information about device
ARGS   :  .X   = file descriptor number
RETURNS:  .A   = device type code (0=console, 1=char-dev, 2=disk-dev)
          .X   = number of columns on device
          .Y   = number of rows per "page" of device
          .CS  = error occurred flag
ALTERS :  errno

This call returns information about the device of an open file.  There are
four possible values for the device type code: 0==console,
1==character-oriented device, and 2==disk device.  The number of rows and
columns per "page" of the device are also returned.  For the console, this
will be the current window size.  For a character-oriented device, it will be
the natural size (typically 80 columns by 66 rows), and for a disk, it will be
40 columns in 64 mode or 80 columns in 128 mode, both by 66 rows.

NAME   :  fdswap
PURPOSE:  swap two file descriptor numbers
ARGS   :  .X   = first file descriptor number
          .Y   = second file descriptor number
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

This call swaps meanings of two file descriptor numbers.  The file descriptors
may be either in use or not use when the call is made.  This call is intended
to be used to redirect the stdin, stdout, and stderr file streams.  To do
this, simply open the new file intended to be, for example, stdout, and swap
the file descriptor number returned from the open with file descriptor number
1 (stdout).  Poof.  Then call your subroutine or external program, and on
return, swap the two file descriptors back, and close the redirection file.

2.4.2. DIRECTORY CALLS

NAME   :  diropen
PURPOSE:  open a directory for scanning its directory entries
ARGS   :  (zp) = directory pathname
RETURNS:  .A   = file descriptor number
          .CS  = error occurred flag
ALTERS :  .X, .Y, errno

This call opens a directory for reading its entries.  It returns a "file"
descriptor number to you to use for reading successive directory entires with
the "dirread" call.  The pathname that you give to this call must be a proper
directory name like "a:" or "c:2//c64/games/:", ending with a colon character.
You can have directories from multiple devices open for reading at one time,
but you cannot have the directory of one device open multiple times.  Also
note that you cannot pass wildcards to this call; you will receive the entire
directory listing.

NAME   :  dirclose
PURPOSE:  close a directory opened for scanning
ARGS   :  .A   = file descriptor number
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Closes a directory that is open for reading.  You can make this call at any
point while scanning a directory; you do not have to finish scanning an entire
directory first.

NAME   :  dirread
PURPOSE:  read the next directory entry from an open directory
ARGS   :  .X   = file descriptor number
RETURNS:  .Z   = end of directory flag
          .CS  = error occurred flag
          aceDirentBuffer = new directory entry data
ALTERS :  .A, .X, .Y, errno

Reads the next directory entry from the specified open directory into the
system interface global variable "aceDirentBuffer" described earlier.  After
opening a directory for reading, the first time you call this routine, you
will receive the name of the disk (or directory).  The "aceDirentNameLen" and
"aceDirentName" fields are the only ones that will contain information; the
rest of the fields should be ignored.

Each subsequent call to this routine will return the next directory entry in
the directory.  All of the "dirent" fields will be valid for these.

Then, after all directory entries have been read through, the last call will
return a directory entry with a null (zero-length) name.  This corresponds to
the "blocks free" line in a Commodore disk directory listing.  The
"aceDirentBytes" field for this last entry will be set to the number of bytes
available for storage on the disk.  On a Commodore disk drive, this will be
the number of blocks free multiplied by 254.  After reading this last entry,
you should close the directory.

At any time, if something bizarre happens to the listing from the disk that is
not considered an error (I don't actually know if this is possible or not),
then the .Z flag will be set, indicating the abrupt ending of the directory
listing.

NAME   :  isdir
PURPOSE:  determine whether the given pathname is for a file or a directory
ARGS   :  (zp) = pathname
RETURNS:  .A   = device identifier
          .X   = is a disk device flag
          .Y   = is a directory flag
          .CS  = error occurred flag
ALTERS :  errno

Given a properly formatted directoryname or filename, this routine will return
whether the name is for a file or a directory, whether the device of the file
or directory is a disk or character device, and the system identifier for the
device.  The two flags return $FF for true and $00 for false.  The device
identifier is superfluous for now, but a "devinfo" call may be added later.
Note that this file does not indicate whether the file/directory actually
exists or not.

NAME   :  chdir
PURPOSE:  change the current working directory
ARGS   :  (zp) = new directory pathname
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Changes the current working directory to the named directory.  Too bad the
Commodore Kernal doesn't have a similar call.  Unlike the "cd" shell command,
the argument has to be a properly formatted directory name.  Note that only
directories in native partitions on CMD devices are supported by this command;
the 1581's crummy idea of partitions is not supported.

NAME   :  cdhome
PURPOSE:  change the current working directory back to the "home" directory
ARGS   :  <none>
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Changes the current working directory back to the "home" directory that is
defined in the "config.sys" file as the initial directory.

NAME   :  mkdir
PURPOSE:  create a new directory
ARGS   :  (zp) = pathname of new directory
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Creates a new directory.  I'm not sure, but I think that the current directory
has to be the parent directory of the directory you want to create.  This may
be required by CMD devices, which will be the lowest common denominator for
directory support.  [Note: in Release #10, this call only accepts a "flat"
directory name].

NAME   :  rmdir
PURPOSE:  delete an empty existing directory
ARGS   :  (zp) = pathname of empty directory to remove
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Deletes an existing directory.  The directory must be empty (have no directory
entries) in order for this command to succeed.  Again, I am pretty sure that
you have to be "in" the parent directory of the one to be deleted, since this
is probably required by CMD devices.  [Note: in Release #10, this call only
accepts a "flat" directory name].

2.4.3. MEMORY CALLS

The calls given in this section are to be used for accessing "far" memory in
ACE, which includes all REU, RAMLink, RAM1 and above, and sections of RAM0
that are not in the application program area.  Applications are not allowed to
access "far" memory directly, because the practice of bypassing the operating
system would undoubtedly lead to problems (can you say "MS-DOS"?).

All of these calls use a 32-bit pointer that is stored in the zero-page
argument field "mp" (memory pointer).  This field is to be interpreted as
consisting of low and high words.  The low word, which of course come first,
is the offset into the memory "bank" that is contained in the high word. Users
may assume that offsets within a bank are continuous, so operations like
addition may be performed without fear on offsets, to access subfields of a
structure, for example.  You may not, however, make any interpretation of the
bank word.  An application should only access far memory that it has allocated
for itself via the "pagealloc" call.

NAME   :  zpload
PURPOSE:  load zeropage storage from far memory
ARGS   :  [mp] = source far memory pointer
          .X   = destination zero-page address
          .Y   = transfer length
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Load zero-page locations with the contents of far memory.  "mp", of course,
gives the address of the first byte of far memory to be retrieved.  The X
register is loaded with the first address of the storage space for the data on
zero page.  It must be in the application zero-page space.  The Y register
holds the number of bytes to be transferred, which, considering that transfers
must be to the application zero-page storage, must be 126 bytes or less.  This
routine will return a "reference through null pointer" if [mp] contains a null
pointer.

NAME   :  zpstore
PURPOSE:  store zeropage data to far memory
ARGS   :  .X   = source zero-page address
          [mp] = destination far memory pointer
          .Y   = transfer length
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

This routine is the complement of "zpload"; this transfers data from zero page
to far memory.  The arguments and restrictions are the same as "zpload".

NAME   :  fetch
PURPOSE:  load near RAM0 storage from far memory
ARGS   :  [mp] = source far memory pointer
          (zp) = destination RAM0 pointer
          .AY  = transfer length
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

This routine will fetch up to 64K of data from far memory into RAM0 memory
where it can be accessed directly by the processor.  The arguments should
mostly speak for themselves.  You should not fetch into RAM0 memory that is
not specifically allocated to the application.  You will get an error if you
try to use a null far pointer.

NAME   :  stash
PURPOSE:  store near RAM0 data to far memory
ARGS   :  (zp) = source RAM0 pointer
          [mp] = destination far memory pointer
          .AY  = transfer length
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

This is the complement of "fetch" and operates analogously, except that it
transfers data from RAM0 to far memory.

NAME   :  pagealloc
PURPOSE:  allocate pages of far memory to current process
ARGS   :  .A   = requested number of pages to be allocated
          .X   = starting "type" of memory to search
          .Y   = ending "type" of memory to search, inclusive
RETURNS:  [mp] = far memory pointer to start of allocated memory
          .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

This routine allocates a given number of contiguous far-memory pages for use
by the application, and returns a pointer to the first byte of the first page.
On calling, the accumulator contains the number of pages to allocate (a page
is 256 contiguous bytes aligned on a 256-byte address (i.e., the low byte of a
page address is all zeros)).

The X and Y registers contain the start and end "types" of far memory to
search for the required allocation.  The possible types are mentioned in the
System Constants section.  The numeric values for the "aceMem" constants are
arranged in order of accessing speed.  So, if your application has speed
requirements that dictate, for example, that RAMLink memory should not be
used, then you would call "pagealloc" with a search range of .X=0 to
.Y=aceMemInternal.  If you wanted to say you are willing to accept any memory
the system can give to you, you would specify .X=0 to .Y=255.  The values of 0
and 255 will be converted to the fastest and slowest memory available.  ACE
will give you the fastest type of memory, from what you specify as acceptable,
that it can.  If you had an application that you didn't want to waste the
high-speed memory on, you could first call "pagealloc" asking for slow memory,
such as .X=aceMemRLREU to .Y=255, and if there is none of that type of memory
left, make another call with .X=0 to .Y=aceMemRLREU-1.

This routine will then search its available free memory for a chunk fitting
your specifications.  If it cannot find one, the routine will return a
"insufficient memory" error and a null pointer.  Note that this error may
occur if there is actually the correct amount of memory free but just not in a
big enough contiguous chunk.  If successful, this routine will return in "mp"
a pointer to the first byte of the first page of the allocated memory.

If you call a subprogram with the "exec" call while the current program is
holding far memory, that far memory will be kept allocated to your program and
will be safe while the child program is executing.  If you don't deallocate
the memory with "pagefree" before exiting back to your parent program, then
the system will automatically deallocate all memory allocated to you.  So,
have no fear about calling "exit" if you are in the middle of complicated far
memory manipulation when a fatal error condition is discovered and you don't
feel like figuring out what memory your program owns and deallocating it.

Some applications will want to have the most amount of memory to work with,
and if there is free space in the application program area that the program is
not using directly, then you may want to use that as "far" memory.  To do
this, you will need to write your own stub routines that manage page
allocation and deallocation requests to the near memory, and calls the
"pagealloc" and "pagefree" routines to manage the far memory.  The "sort"
program distributed with ACE does this.  Please note that you CANNOT simply
free the unused memory of the application program area and expect the system
to manage it.  Bad stuff would happen.

Some applications will want to have a byte-oriented memory allocation service
rather than a page-oriented service.  You can build a byte-oriented service on
top of the page-oriented service in your application programs that manage
memory for the application and ask the system for pages whenever more memory
is required by the application.  Note that this still means that allocated
memory will be freed automatically when an application exits.  The "sort"
program implements this byte-oriented service, so you can check its source
code to see how this is done (or to simply cut and paste the code into your
own program).

NAME   :  pagefree
PURPOSE:  free pages of far memory allocated to current process
ARGS   :  [mp] = far memory pointer to start of memory to be freed
          .A   = number of pages to be freed
RETURNS:  .CS  = error occurred flag
ALTERS :  [mp], .A, .X, .Y, errno

This deallocates memory that was allocated to a process by using the
"pagealloc" system call.  You will get an error return if you try to
deallocate memory that you don't own.

2.4.4. SCREEN CONTROL CALLS

This section describes the system calls that are available to application
programmers for full-screen applications.  These calls are intended to be
general enough to handle different screen hardware (the VIC and VDC chips and
a VIC soft-80-column bitmap screen, and possibly others).  These calls are
also designed to be efficient as possible, to discourage progammers from
attempting to bypass using them.  Bypassing these calls would be a bad thing.

The calls are designed around the C-128/PET concept of a window.  There is
only one active window on the display at a time, which may be is large as the
entire screen or as small as 1x1 character cells.  This window is very cheap
to setup and tear down.  An application can have multiple windows on the
screen by switching the active window around.

In the calls below, all mention of "sw" in the arguments and return values
refer to the "syswork" array.  For many calls, there is a "char/color/
high-attribute" argument.  This argument determines which parts of a screen
location will be modified.  There are three components to each screen
location: the character code, the color code, and the high-attributes.  The
character code is exactly the same as the PETSCII code for the character that
you want to display (unlike the screen-code arrangement that Commodore chose).
There are 128 individual characters in the normal PETSCII positions, and 128
reversed images of the characters in the most sensible other positions.  The
codes are as follows:

CODES (hex)   DESCRIPTION
-----------   -----------
$00-$1f       reverse lowercase letters
$20-$3f       digits and punctuation
$40-$5f       lowercase letters
$60-$7f       reverse graphics characters
$80-$9f       reverse uppercase letters
$a0-$bf       graphics characters
$c0-$df       uppercase letters
$e0-$ef       reverse digits and punctuation

There are sixteen color codes, occupying the lower four bits of the color
value.  These are RGBI codes, as follows:

CODE(dec)   (hex)   (bin)   DESCRIPTION
---------   -----   -rgbi   -----------
        0      $0   %0000   black
        1      $1   %0001   dark grey
        2      $2   %0010   blue
        3      $3   %0011   light blue
        4      $4   %0100   green
        5      $5   %0101   light green
        6      $6   %0110   dark cyan on VDC, medium grey on VIC-II
        7      $7   %0111   cyan
        8      $8   %1000   red
        9      $9   %1001   light red
       10      $a   %1010   purple
       11      $b   %1011   light purple on VDC, orange on VIC-II
       12      $c   %1100   brown
       13      $d   %1101   yellow
       14      $e   %1110   light grey
       15      $f   %1111   white

Finally, there are the high-attribute bits.  These occupy the four most
significant bits of the color value.  Depending on the type of display (VIC
text, VDC text, or VIC/VDC bitmap), these bits have one of three meanings:
character attributes, background character color, or no effect.  Thus, care
must be taken in using these bits; they will have different effects on
different displays.  The background color codes are the same as the foreground
color codes listed above.  The character attributes have the following
meanings:

BIT VALUE   (dec)   (hex)   DESCRIPTION
-avub----   -----   -----   -----------
%10000000     128     $80   alternate characterset (italic)
%01000000      64     $40   reverse character
%00100000      32     $20   underline
%00010000      16     $10   blink

These values are additive (or, should I say, "or-ative"); you can use any
combination of them at one time.  Normally, you may wish to leave the
high-attribute bits alone, unless you take the values to give them from the
color palettes (next section).  To specify which of you wish to have changed,
set bits in the "char/color/high-attribute" argument to system calls.  The
flags have the following values.  They are or-ative as well:

BIT VALUE   (dec)   (hex)   DESCRIPTION
-cah-----   -----   -----   -----------
%10000000     128     $80   modify character
%01000000      64     $40   modify color
%00100000      32     $20   modify high-attribute bits

The screen calls that deal with placing characters on the screen refer to
screen locations using absolute addresses of locations in screen memory.  This
scheme is used for increased efficiency.  You can obtain information about the
absolute screen address of the top left-hand corner of the current window and
the number of screen addresses between successive rows, to figure out screen
addresses for your applications.  For added convenience, there is a call which
will accept row and column numbers and return the corresponding absolute
screen address.  Each successive column of a row has an absolute screen
address that is 1 higher than the previous, for all displays.

The screen-control system calls are as follows:

NAME   :  winmax
PURPOSE:  set window to maximum size
ARGS   :  <none>
RETURNS:  <none>
ALTERS :  .A, .X, .Y

Sets the current window to cover the entire screen.

NAME   :  winclear
PURPOSE:  clear window
ARGS   :  .A   = char/color/high-attribute modification flags
          .X   = character fill value
          .Y   = color fill value
RETURNS:  <none>
ALTERS :  .A, .X, .Y

This call "clears" the current window by filling it with the character/color
you specify.  You can use the char/color/hi-attr to limit what gets cleared.

NAME   :  winset
PURPOSE:  set dimensions of window
ARGS   :  .A   = number of rows in window
          .X   = number of columns in window
          sw+0 = absolute screen row of top left corner of window
          sw+1 = absolute screen column of top left corner of window
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

Sets the current window to the size you specify.  You will get an error return
if the window will not fit on the screen or of it does not contain at least
one character.

NAME   :  winsize
PURPOSE:  return dimensions of window
ARGS   :  <none>
RETURNS:  .A   = number of rows in window
          .X   = number of columns in window
          sw+0 = absolute screen row of top left corner of window
          sw+1 = absolute screen column of top left corner of window
         (sw+2)= screen address of top left corner
         (sw+4)= screen address increment between successive rows on screen
ALTERS :  <none>

Returns information about the current window.

NAME   :  winput
PURPOSE:  put characters and color onto screen
ARGS   : (sw+0)= absolute screen address to start putting data at
         (sw+2)= character string pointer
          .X   = length of character string
          .Y   = color
          .A   = char/color/high-attribute modification flags
          sw+4 = fill character
          sw+5 = total field length
RETURNS:  <none>
ALTERS :  .A, .X, .Y

Puts text onto the screen.  The output region is given by the absolute
starting screen address and the total field length.  This region must be
contained on one line of the current window, or bad things will happen.  A
pointer to the characters to be printed is given, as well as the length of the
character array.  Control characters in this string are ignored; they are
poked literally onto the screen, including the null character.  The length of
the character string must be less than or equal to the total length of the
field.  Remaining spaces in the field will be filled in with the "fill
character".

The color of the total field length will be filled in with "color".  You can
use the "char/color/hi-attr" modification flags to specify what is to be
changed.  If you were to, for example, specify that the colors of the field
are not to be changed, then the call would execute faster.

NAME   :  wincolor
PURPOSE:  set screen and border colors
ARGS   :  .X   = new RGBI screen color
          .Y   = new RGBI border color
          .A   = which colors to change ($80=screen + $40=border)
RETURNS:  .X   = resulting RGBI screen color
          .Y   = resulting RGBI border color
ALTERS :  .A

Sets the color of the screen and border.  You may optionally set one, the
other, both, or neither.  The resulting colors for colors changed, and the
existing colors for colors unchaned will be returned.  Note that not all
screens have an adjustable color, so the border argument may be ignored.

NAME   :  winpos
PURPOSE:  return screen address of given row and col
ARGS   :  .A   = row
          .X   = column
RETURNS: (sw+0)= screen memory address of position
ALTERS :  .A, .X, .Y

Given a row and column in the current window, returns the corresponding
absolute screen memory location for use with other calls.  No errors are
returned, so garbage in, garbage out.

NAME   :  wincursor
PURPOSE:  activate/deactivate cursor
ARGS   : (sw+0)= screen address to place cursor
          .A   = enable flag ($ff=cursor-on / $00=cursor-off)
          .Y   = color to show cursor in
RETURNS:  <none>
ALTERS :  .A, .X, .Y

Displays or undisplays the cursor at the given screen address.  This call
returns immediately in either case.  No errors are returned.  Do not display
anything in or scroll the window while the cursor is being displayed, do not
display the cursor twice, and do not undisplay the cursor twice in a row or
bad things will happen.  Also, make sure you give the same address when
undisplaying the cursor as you did when displaying the cursor.  When the
system starts, the cursor will be in its undisplayed state (duh!).  You also
get to specify the color you want the cursor to be shown in.  The
high-attribute bits of this color are ignored.

NAME   :  winscroll
PURPOSE:  scroll window
ARGS   :  .A   = flags: char/color/hi-attr + $08=up + $04=down
          .X   = number of rows to scroll up/down
          sw+4 = fill character
          .Y   = fill color
RETURNS:  <none>
ALTERS :  .A, .X, .Y

Scrolls the contents of the current window up or down.  You can scroll any
number of rows at a time.  After scrolling, the bottom (or top) rows will be
filled with the fill character and color.  You can limit whether the
characters and/or colors are to be scrolled by using the "flags" byte in the
usual way.  Scrolling only the characters, for example, will be twice as fast
as scrolling both characters and attributes.  Whether to scroll up or down is
specified also using bits in the "flags" field, as indicated in the input
arguments above.  You can specify scrolling in more than one way, and the
result will be to scroll in each specified direction in turn, in the order up,
then down.  In the future, scrolling left and right may be added to this call.
[Note: in Release #10, scrolling the screen downward is not implemented.]

2.4.5. CONSOLE CALLS

The calls in this section refer to the system "console", which includes the
screen and keyboard.  The screen-related calls are at a higher level than the
calls in the previous section.

NAME   :  conread
PURPOSE:  read input line from console
ARGS   :  (zp) = pointer to buffer to store data into
          .AY  = maximum number of bytes to read
RETURNS:  .AY  = (zw) = number of bytes actually read in
          .ZS  = EOF reached flag
ALTERS :  .X

Same as the "read" system call, except this always reads from the console, and
there are no errors.

NAME   :  conwrite
PURPOSE:  write data to console
ARGS   :  (zp) = data to print
          .AY  = bytes of data to print
RETURNS:  <none>
ALTERS :  .A, .X, .Y, errno

Same as the "write" system call, except this always writes to the console, and
no errors are possible.

NAME   :  conputchar
PURPOSE:  write character to console
ARGS   :  .A   = character
RETURNS:  <none>
ALTERS :  .A, .X, .Y, errno

Write a single character to the console.  Control characters are interpreted
as per usual.  The control characters are as follows:

CODE(hex)   CODE(dec)   NAME   DESCRIPTION
---------   ---------   ----   -----------
$07         7           BEL    ring the bell
$09         9           TAB    move cursor to next 8-char tab stop
$0a         10          LF     move cursor to beginning of current line
$0d         13          CR     go to start of next line
$14         20          BS     non-destructive backspace
$93         147         CLR    clear the screen

NAME   :  conputlit
PURPOSE:  write literal character to console
ARGS   :  .A   = character
RETURNS:  <none>
ALTERS :  .A, .X, .Y, errno

Same as the "conputchar" system call, except that control characters are not
interpreted.

NAME   :  stopkey
PURPOSE:  check if stop key is being held down
ARGS   :  <none>
RETURNS:  .CS  = stop key pressed
ALTERS :  .A, .X, .Y, errno

Indicates whether the STOP (RUN/STOP) key is currently being held down by the
user.  If so, carry flag is set on return (and clear if not).  If the stop key
is discovered to be pressed by this call, then the keyboard buffer will also
be cleared.

NAME   :  getkey
PURPOSE:  get a key code from the keyboard buffer
ARGS   :  <none>
RETURNS:  .A   = keyboard character
ALTERS :  .X, .Y

Waits for the user to type a key (or takes a previous keystroke from the
keyboard buffer).  Regular characters are returned in their regular PETSCII
codes, but there are many special control keystrokes.  I still haven't figured
out what all of the special codes should be, but all 256 possible character
values will be covered.  Special codes like "page up", etc. should help in
standardizing control keystrokes for applications.  Note that these
definitions of keycodes is only suggested; your full-screen application can
interpret them however it wants.  The key code is returned in the accumulator.
No errors are possible.

The tables below summarize the meanings of the various key codes.  Not all of
the C64 keys have been decided yet.  Note that the keys for "@" to "_", used
in association with shifting keys, are "@ABCDEFGHIJKLMNOPQRSTUVWXYZ[\]^_".
"CT" means Control, "SH" means Shift, "AL" means Alternate, and "CO" means
Commodore.  I haven't decided how to define Alternate on a C64 yet.

CODE(s)   C128 KEY(s)    C64 KEY(s)     DESCRIPTION
-------   ------------   ------------   -----------
$20-$3f   SPACE to "?"   SPACE to "?"   Regular numbers and punctuation
$40-$5f   "@" to "_"     "@" to "_"     Regular lowercase letters
$60-$7f   AL-@ to AL-_   <undecided>    Alternate keys
$a0-$bf   CO-@ to CO-_   CO-@ to CO-_   Commodore keys
$c0-$df   "`" to HOUSE   "`" to HOUSE   Regular uppercase letters
$e0-$ef   CT-@ to CT-_   CT-@ to CT-_   Control keys

CODE(s)   C128 KEY(s)    C64 KEY(s)     DESCRIPTION
-------   ------------   ------------   -----------
$00       <none>         <none>         <cannot be generated>
$01       CT-RETURN      CT-RETURN      EOF
$02       SH-TAB         <undecided>    Backtab
$03       STOP           STOP           Stop some operations
$04       SH-HELP        <undecided>    Context-insensitive help
$05       CT-2           CT-2           White
$06       SH-LEFT        <undecided>    Word left
$07       SH-LINEFEED    <undecided>    <undecided>
$08       CO-DEL         CO-DEL         Rubout character under cursor
$09       TAB            <undecided>    Tab
$0a       LINEFEED       <undecided>    Linefeed
$0b       SH-RIGHT       <undecided>    Word right
$0c       CO-UP          <undecided>    Goto top of document
$0d       RETURN         RETURN         Return
$0e       SH-ESCAPE      <undecided>    <undecided>
$0f       CO-DOWN        <undecided>    Goto bottom of document
$10       CO-LEFT        <undecided>    Goto beginning of line
$11       DOWN           DOWN           Cursor down
$12       CT-9           CT-9           Rvs
$13       HOME           HOME           Home
$14       DEL            DEL            Backspace
$15       CO-RIGHT       <undecided>    Goto end of line
$16       CT-UP          <undecided>    Page up
$17       CT-DOWN        <undecided>    Page down
$18       CT-TAB         <undecided>    <undecided>
$19       CT-LEFT        <undecided>    Page left
$1a       CT-RIGHT       <undecided>    Page right
$1b       ESCAPE         <undecided>    Escape
$1c       CT-3           CT-3           Red
$1d       RIGHT          RIGHT          Cursor right
$1e       CT-6           CT-6           Green
$1f       CT-7           CT-7           Blue

CODE(s)   C128 KEY(s)    C64 KEY(s)     DESCRIPTION
-------   ------------   ------------   -----------
$80       CT-F1          CT-F1          Function key 9
$81       CO-1           CO-1           Orange/Purple(?)
$82       CT-F3          CT-F3          Function key 10
$83       SH-STOP        SH-STOP        <undecided>
$84       HELP           <undecided>    Context-sensitive help
$85       F1             F1             Function key 1
$86       F3             F3             Function key 3
$87       F5             F5             Function key 5
$88       F7             F7             Function key 7
$89       SH-F1          SH-F1          Function key 2
$8a       SH-F3          SH-F3          Function key 4
$8b       SH-F5          SH-F5          Function key 6
$8c       SH-F7          SH-F7          Function key 8
$8d       SH-RETURN      SH-RETURN      <undecided>
$8e       CT-F5          CT-F5          Function key 11
$8f       CT-F7          CT-F7          Function key 12
$90       CT-1           CT-1           Black
$91       UP             UP             Cursor up
$92       CT-0           CT-0           Rvs off
$93       SH-HOME        SH-HOME        Clear screen
$94       SH-DELETE      SH-DELETE      Insert one space
$95       CO-2           CO-2           Brown
$96       CO-3           CO-3           Light red
$97       CO-4           CO-4           Dark gray
$98       CO-5           CO-5           Medium gray/dark cyan(?)
$99       CO-6           CO-6           Light green
$9a       CO-7           CO-7           Light blue
$9b       CO-8           CO-8           Light gray
$9c       CT-5           CT-5           Magenta
$9d       LEFT           LEFT           Cursor left
$9e       CT-8           CT-8           Yellow
$9f       CT-4           CT-4           Cyan

NAME   :  concolor
PURPOSE:  set the console main text and cursor colors
ARGS   :  .A   = which colors to modify: $02=character + $01=cursor 
                 + $20=modify high-attributes of colors
          .X   = new RGBI character color
          .Y   = new RGBI cursor color
RETURNS:  .X   = resulting character color
          .Y   = resulting cursor color
ALTERS :  .A

Sets the character and cursor colors to be used by the console for the "read"
and "write" system calls that refer to files opened to the console device. You
can use the flags argument to limit what gets changed.

NAME   :  conpalette
PURPOSE:  get standard color palette for current screen
ARGS   :  <none>
RETURNS:  sw+0 = main character color
          sw+1 = cursor color
          sw+2 = status character color
          sw+3 = separator character color
          sw+4 = highlight character color
          sw+5 = alert character color
          sw+6 = screen border color
          sw+7 = screen background color
ALTERS :  .A, .X, .Y

Returns the palette of colors that are recommended to be used in applications.
These colors are chosen by the user in the system configuration, so they can
be interpreted as being what the user wants and expects applications to use. A
different selection is made by the user for each different screen type, and
the palette returned will be for the screen type currently in use.  The
high-attribute bits of these colors are valid.  Eight colors are included in
the palette, and you may interpret their meaning according to the application.
The suggested usages are given in the return arguments listed above.

NAME   :  conscreen
PURPOSE:  set the screen size
ARGS   :  .A   = number of text rows required, minimum
          .X   = number of text columns required, minimum
RETURNS:  .A   = number of text rows you get
          .X   = number of text columns you get
          .CS  = error occurred flag (requested size cannot be given)
ALTERS :  .Y, errno

This call selects an appropriate display device, screen, and layout for
displaying text.  You ask for the minimum number of rows and columns you
require on the screen, and the call returns to you what you receive.  If the
system cannot match your minimum requirements, an error will be returned, and
the current screen will be unchanged.  The clock speed of the processor will
be changed to match the screen selected, if appropriate.  If you pass either
number of rows or columns as 0, then the system default value for the current
screen type will be used.  If you pass either parameter having value 255, then
the system will use the maximum possible value.

NAME   :  conpos
PURPOSE:  set cursor location
ARGS   :  .A   = row
          .X   = column
RETURNS:  .CS  = error encountered flag
ALTERS :  .A, .X, .Y

This call will set the screen location that the next console "read" or "write"
system call will operate from.  If the "cursor" position is outside the
boundaries of the current window on the screen, an error will be returned.

2.4.6. PROCESS CONTROL CALLS

This section describes calls that are used to control the execution of
processes (active programs).  From within one program, you can call for the
execution of another program, have it execute, and then return to the calling
program.  Since only one program is allowed in memory at a time, some special
problems arise.

NAME   :  exec
PURPOSE:  execute external program as a child process
ARGS   :  (zp) = program name of executable
          (zw) = start address of argument vector
          .AY  = number of arguments
          [mp] = pointer to far memory volatile storage
RETURNS:  .A   = exit code
          .X   = number of bytes in "aceExitData" used
          (zp) = given argument count
          (zw) = given argument vector pointer
          [mp] = pointer to far memory volatile storage
          .CS  = error occurred flag
ALTERS :  .Y, errno

Calling this routine will cause a new "frame" to be set up on the "system
stack" (lowering the available application area memory a little), the
specified program to be loaded into memory over top of the current one, the
new program to be executed, the old program to be reloaded from whatever disk
unit it came from originally upon exit of the new program, and control to be
returned to the old process with the return values from the executed program.
This is a complicated procedure and many things can go wrong.

The first thing that a process that wants to call another program must do is
set up the arguments to be passed in.  All arguments must be null-terminated
strings.  These arguments are to be put into high memory, starting from one
less than the location pointed to by "aceMemTop" and working downward.  It
does not matter in which order the strings are placed, as long as they are all
grouped together.  Then, immediately below the strings comes the vector of
two-byte RAM0 pointers that point to the strings.  This array must be in
order, with the lowest entry pointing to the first (zero subscript) string,
etc., the second highest entry pointing to the last string, and the highest
entry containing the value $0000.  An asciigram follows:

  HIGHER ADDRESSES
|           |
|           | <--(aceMemTop)
+-----------+
|           |
| string    |
|           |         : collection of null-terminated strings
|  contents |
|           |
|           |
+-----------+
|   $0000   |         : argv[N] : null argument pointer
+-----------+
| strptrN-1 |         : argv[N-1]
+-----------+
| strptrN-2 |         : argv[N-2]
+-----------+
.           .
.           .
+-----------+
| strptr 1  |         : argv[1] : first actual argument
+-----------+
| strptr 0  | <--(zw) : argv[0] : filename of program to be executed
+-----------+
|           |
  LOWER ADDRESSES

The first entry should indicate the filename or command name of the program
being executed, and the subsequent arguments are the actual input arguments to
the program being called.  The address of the first argument vector table
entry is loaded into (zw), and the number of arguments is loaded into .AY.
Note that this value also includes the command name, so if, for example, you
were to call program "wc" to count two filenames "hello" and "goodbye", then
you would pass an argument count of 3.  The name pointed to by "argv[0]" does
not actually have to be the literal command name, but the one pointed to by
(zp) does.  If a relative executable name is given in (zp), then the search
path will be used to locate the executable.  Oh, don't screw up the
organization of the arguments or bad things will happen; there is no structure
checking.

After setting up the arguments, you'll want to set up any redirections of
stdin, stdout, or stderr you'll be needing.  Because there is only one open
file table in the whole uni-tasking system, you'll have to manipulate existing
entries using the "fdswap" system call described earlier.  The open file table
is inherited by the child process.  Note that if it closes any of the open
files it inherited, then they are also closed to your use also.  If the child
accidentally leaves open any files it opened, they will be closed by the
system before you are reactivated.

Finally, before the call is made, you have to save any volatile local
information into "far" memory.  All application zeropage and application area
memory will be modified by the called program, so you must save whatever you
will need to continue after the return to be able to continue.  As mentioned
earlier, all of the "far" memory that a parent program owns will be safe, so
you can save your volatile information there, in any format you wish.  All you
have to do is save the pointer to the far memory into the [mp] pointer.  Upon
return of the child process, the value you put into [mp] will be restored, and
you can then restore your volatile information out of far storage.  If you
wish to save no volatile information, then you can just leave garbage in the
[mp] value, since it will not be interpreted by the system.

Alright, so now you call the "exec" primitive, the child program is loaded,
executed, and it returns.

At this time, the parent program (that's you) is reloaded from wherever it was
loaded originally and you are returned to the instruction immediately
following the "jsr exec", with your processor stack intact but the rest of
your volatile storage invalid.  Even if there is an error return (carry flag
set), your volatile storage will still need to be restored, since the
application area may have been overwritten before the error was discovered.
In the case of an error return, the child process will not have been executed.
If the system is unable to reload the parent program (you), then an error
return is given to your parent, and so on, as far back as necessary.  (This is
a minor exception to the rule that an error return indicates that a child
didn't execute; in this case, the child didn't complete).

You are also returned an "exit code", which will have application-specific
meaning, although standard programs (e.g., shell script) interpret the value
as: 0==normal exit, anything else==error exit.  The X register is also set to
indicate the amount of "aceExitData" that is used, to allow for more
complicated return values.  [Note: this call is still not implemented in
Release #10.]

NAME   :  execsub
PURPOSE:  execute internal subroutine as a separate process
ARGS   :  (zp) = address of subroutine
          (zw) = address of argument vector
          .AY  = argument count
          [mp] = far memory pointer
RETURNS:  .A   = exit code
          .X   = number of bytes in "aceExitData" used
          (zp) = given argument count
          (zw) = given argument vector pointer
          [mp] = given far memory pointer
          .CS  = error occurred flag
ALTERS :  .Y, errno

This call is very similar to "exec", except that it calls an internal
subroutine rather than an external program.  Thus, you don't have to save or
restore your volatile storage, or worry about loading the child or reloading
the parent.  You do, however, set up the arguments and file redirections as
you would for a full "exec".

NAME   :  exit
PURPOSE:  exit current program, return to parent
ARGS   :  .A   = exit code
          .X   = number of bytes in "aceExitData" used
RETURNS:  <there is no return, brah-ha-ha-ha-ha-ha!!!>
ALTERS :  <don't bloody well matter to you>

This call causes the current program to exit back to its parent. A program
that exits simply by returning to its environment will give back an exit code
of 0, which should be interpreted as a normal return.  If you wish to indicate
a special return, you should use some exit code other than zero.  Many
utilities will interpret non-zero error codes as actual errors and may abort
further operations because of this.

You may set up a return data in "aceExitData", up to 255 bytes worth, and load
the number of bytes used into .X if you wish.  It is recommended that the
first field of this data be a special identifier code so programs that cannot
interpret your data will not try.  You cannot give any far pointers in your
return data, since all far memory allocated to you will be freed by the system
before returning to your parent.

NAME   :  memstat
PURPOSE:  get "far" memory status plus process id
ARGS   :  .X   = zero-page address to store status information
RETURNS:  .A   = current process id
         [.X+0]= amount of "far" memory free
         [.X+4]= total amount of "far" memory
ALTERS :  .X, .Y

This call returns the current process id, the number of bytes of far memory
currently free, and the total amount of far memory.

2.4.7. MISCELLANEOUS CALLS

NAME   :  utoa
PURPOSE:  convert unsigned 32-bit number to a decimal PETSCII string
ARGS   :  .A   = minimum length for return string
          .X   = zero-page address of 32-bit number
          (zp) = pointer to string buffer to store string
RETURNS:  .Y   = length of string
ALTERS :  .A, .X

This is a utility call in the kernel.  It is really not necessary for it to be
in the kernel, but so many programs make use of it that it makes sense for it
to be factored out.  You give a pointer to a 32-bit unsigned value in zero
page memory, a pointer to a buffer to store that string that is at least as
long as necessary to store the value plus the null-character terminator that
will be put on the end of the string, and a minimum length value for the
string.  If the number requires fewer digits than the minimum length, the
string will be padded with spaces on the left.  Since a 32-bit quantity can
only contain an maximum of ten decimal digits, the string buffer will only
need to be a maximum of eleven bytes in size.

NAME   :  getdate
PURPOSE:  get the current date and time
ARGS   : (.AY) = address of buffer to put BCD-format date into
RETURNS:  <none>
ALTERS :  .A, .X, .Y

Returns the current date and time in the BCD format described in the paragraph
on "aceDirentDate".  It puts it into the at-least-eight-byte storage area
pointed to by (.AY).

NAME   :  setdate
PURPOSE:  set the current date and time
ARGS   : (.AY) = address of date in BCD format
RETURNS:  <none>
ALTERS :  .A, .X, .Y

Sets the current date and time in the system.  (.AY) points to the BCD date
string whose format is discussed in the paragraph on "aceDirentDate".  No
validity checking is performed on the date given.

NAME   :  cmdopen
PURPOSE:  open command channel to Commodore disk drives
ARGS   :  (zp) = device name
RETURNS:  .A   = file descriptor number
          .CS  = error occurred flag
ALTERS :  .X, .Y, errno

This "cmd" set of system calls really should not be present, but they will be
needed until the full complement of disk-utility system calls are implemented.
It is really not recommended that any application program rely on these calls
being around very long.  This call opens the command channel on the named
device (standard ACE device name string) and returns the file descriptor
number to use thereafter.

NAME   :  cmdclose
PURPOSE:  close command channel to Commodore disk drives
ARGS   :  .A   = file descriptor number
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

This closes an opened command channel to a disk drive.  Closing the status
will NOT affect any other open files on the disk unit at the time.

NAME   :  cmdsend
PURPOSE:  send command over command channel to Commodore disk drives
ARGS   :  .X   = file descriptor number
         (.AY) = pointer to null-terminated command string
RETURNS:  .CS  = error occurred flag
ALTERS :  .A, .X, .Y, errno

This sends a command string to a disk drive.  Since a null-terminated string
representation is used, not all Commodore/CMD-DOS commands can be sent, but
the important ones can be.

NAME   :  cmdstatus
PURPOSE:  receive current status from command channel of Commodore disk drives
ARGS   :  .X   = file descriptor number
         (.AY) = pointer to buffer for null-terminated status string
RETURNS:  .A   = status code in binary
          .CS  = error occurred
ALTERS :  .X, .Y, errno

This returns the status of a disk drive in a string as well as the binary disk
status number in the accumulator.  The given status buffer must be at least 50
or so characters long (whatever is the longest possible disk status string).

3. USER PROGRAM ORGANIZATION

The ACE system itself is written using the Buddy-128 assembler, so it is
recommended that applications be written in this also.  User programs for ACE
have a very simple structure.  Here is the standard "hello, world" example
program written in Buddy assembler for ACE:

-----=-----
.seq acehead.s
.org aceAppAddress
.obj "@0:hello"

jmp main
.byte aceID1,aceID2,aceID3
.byte 64,0

main = *
   lda #<helloMsg
   ldy #>helloMsg
   sta zp+0
   sty zp+1
   lda #<helloMsgEnd-helloMsg
   ldy #>helloMsgEnd-helloMsg
   ldx #stdout
   jsr write
   rts

helloMsg = *
   .asc "Hello, cruel world."
   .byte 13
helloMsgEnd = *
-----=-----

This would normally be put into a file called "hello.s".  The ".s" extension
means that this is an assembler file (a la Unix).  The first thing this
program does is include the "acehead.s" file.  This is the Buddy assembler
file that contains the header information declarations required to access the
ACE system interface.  The next line gives the start address to start
assembling to; it must be "aceAppAddress", which is the address that ACE will
load the program at.  The next line is a directive to the assembler to write
the executable code to a Commodore-DOS "PRG" file named "hello".  This will be
the command to enter at the ACE shell prompt.

The next eight bytes of object code (which are the first eight bytes of a
loaded program) describe the header required by ACE programs.  The first three
bytes must be a JMP to the main routine of the program.  The next three bytes
must have the values "aceID1", "aceID2", and "aceID3", respectively.  The next
two bytes are the minimum stack requirements and flags, respectively.  The
stack requirement is for the processor stack, and ACE will make sure your
program has at least this much space before your program starts.  The flags
field is currently undefined, but you must give it a value of 0.  And that's
all there is to it.  The rest of the program can be organized however you want
it to be.

In this example, we set up the arguments for the "write" system call to print
the string "Hello, cruel world." plus a carriage return to standard output.
Note that this string does not need a terminating null ($00) character since
the write call takes a buffer length.  The program then returns to its calling
environment via an RTS.  This will cause an implied "exit(0)" to be performed
by the system, returning to the parent program.

Although this program does not take advantage of this, an application program
may use zero-page locations $0002 through $007f for storage without fear of
having the storage trodden upon by the system.

Finally, an application program starts at location "aceAppAddress" (plus six)
and is allowed to use memory all the way up to one byte less than the address
pointed to by "aceMemTop" for its own purposes.  Currently, this amount of
space is on the order of magnitude of about 20K.  This will be increased in
the future.

Application programs are not to access I/O features or even change the current
memory configuration during execution.  All I/O and other unusual contortions
must be performed by ACE system calls; otherwise, we could end up in as bad a
shape as MESS-DOS.

4. CONCLUSION

Cool, eh?
-----------------------------------------------------------------------=END=--